## Slide 1
PARTNERS IN DAMAGE PREVENTION
2026

## Slide 2
WALK A MILE IN OUR SHOES
Our goal is to work together to reduce damages, down time on projects, and improve safety standards.
Let’s work together to build stronger relationships and safer sites for everyone.

## Slide 3
In all 5 states, tickets expire if excavation does not commence by the 30th day from the date of issue. Renew tickets online with Exactix or by calling 811.
  MA, NH, and VT – 30 days
  ME - 60 days, but work must start within 30 days
  RI - Tickets do not expire if the marks are maintained.
Ticket Expiration Times

## Slide 4
Dates
Ticket Start Dates: We must respond within
  72 business hours in MA, ME, NH, VT and RI
  Weekend and holidays don’t count toward the start date

## Slide 5
Dates
Remarks: Remark notices can be submitted if marks are faded and your ticket is still valid
  48 business hours in RI
  72 business hours in VT (new ticket)
  72 business hours in New Hampshire (new ticket)
  24 business hours in MA and ME
  Tickets do not expire in RI

## Slide 6
In Reference Notice
  Call 811 to have a message sent out regarding an existing ticket
  Report no marks
  Ask for clarification of marks
  Add sub-contractor
  Provide additional location information

## Slide 7
Once you get your work order you should complete the following steps.
Visit the site
Pre-mark entire work area, including all poles on the ticket if for pole replacements
Make sure your pre-marks match the entire scope of work
Ticket Process: Start to Finish

## Slide 8
Ticket Process: Start to Finish
4. Submit a ticket with Exactix at DigSafe.com or by calling 811
5. Include Contact Info of the FIELD PERSON on the ticket:
  Phone number
  Email address
  Alternate phone number
6. Give Description of Jobsite Location:
  Address or address range with building/house number
  GPS Coordinates
  Place names, pole numbers, between cross streets

## Slide 9
Putting too much on one ticket
  Too many poles
  Entire neighborhoods
  Town line to Town line
Not enough information on the ticket
Large projects in stages
Correct contact information
Pre-marking
Submitting tickets too early
Ticket Mistakes to Avoid

## Slide 10
Long Mark outs

## Slide 11
Updating the pre-marks when requesting renewals
Submit a new ticket rather than request remarks
Maintaining previous marks
Renewals & Ongoing Projects

## Slide 12
Contractor Responsibilities
Remember that the excavator is responsible for maintaining the marks for 30 days
Use the appropriate paint color and type of markings when you are maintaining the marks
Take pics/videos before any work takes place

## Slide 13
Pre-marks are required for all tickets
2. Required to be completed prior to submitting ticket
Must be marked in white paint, stakes, ribbons or flags.
                In winter time use Pink paint for Pre-marks
4. Label with contractor name or initials
Importance of Pre-Marks

## Slide 14
Bad pre-marks

## Slide 15
Good Pre-Marks

## Slide 16
Pre-marked
Marked
Notes: Pole on the left is pre-marked with white tape. Pole on the right is marked with flags.

## Slide 17
If you see any of these structures with no markings, call before you dig.

## Slide 19
Single Direct Buried Cables with Tolerance Zones (18”)

## Slide 20
Multiple Direct Buried With Tolerance Zones (18”) and Duct Structure Marks

## Slide 21
Gas Service and Offset Marks

## Slide 22
Private vs Public Utilities

## Slide 23
Private vs Public Utilities

## Slide 24
Who Owns That?
For Example:
Electrical Lines after the meter
Sewer Laterals/Services
Water services after the service valves
Most lighting in parking lots/businesses
Most Schools/Universities and Hospitals
  Steam lines, propane, O2, drainage

## Slide 25
How we can help each other
Communication is Key
If something doesn’t look right, or you don’t see any markings on site, make a phone call
Be willing and prepared to answer questions about a site.
Try to have two or more methods of communication on your ticket (Email/multiple phone numbers)
Have distinct and identifiable pre-marks at your job site

## Slide 26
How we can help each other
Try to stagger the tickets that you submit.
Tickets for multiple large jobs submitted at once is very difficult to complete on time
One or two poles/anchors per ticket, rather than 8-10
Break down tickets for large jobs in sections, rather than all in one ticket.

## Slide 27
How we can help each other
It’s good practice to have a copy of the ticket info on site because:
  Multiple locators will arrive on site to respond to different utilities
  Great way to track which utilities have already marked/cleared the site

## Slide 28
What you can expect from us
Safe Excavation
On-time quality locates
Less extensions
Less damages
Less work stoppages

## Slide 30
d) Excessive notifications by the same excavator on the same day may constitute extraordinary circumstances causing an operator to be unable to designate the location of underground facilities in a timely manner as required in En 806.02. It shall be presumed to be an extraordinary circumstance causing an operator to be unable to designate the locations of underground facilities as required in En 806.02 when the same excavator makes in excess of 15 notifications on the same day, provided that the operator complies with En 806.01(g) with respect to the notifications in excess of 15.
NH RULE CHANGE

## Slide 31
Points of Contact
  (207) 852-8315
(317) 575-7800