## Slide 1
MUST Breakfast Seminar
Delta Hotels By Marriott Burlington
1117 Williston Road, South Burlington, VT

## Slide 2: Engineering Division
The Engineering Division specializes in electricity, nuclear power, pipeline safety (natural gas and propane), and underground damage prevention.
Bill Jordan – Director
Lindsey Wells – Admin. Services Coordinator

## Slide 3: Vermont Statutes and Rules
Statute - 30 V.S.A. Chapter 86 Underground Utility Damage Prevention System
Public Utility Commission Rule 3.800 Underground Utility Damage Prevention

## Slide 4: Definition of “Excavation Activities”
30 V.S.A. § 7001(4)
"Excavation activities" means any activities
Disturb the subsurface of the earth or could damage underground utility facilities and that may involve the removal of earth, rock, or other materials in the ground or
the demolition of any structure by the discharge of explosives or
the use of powered or mechanized equipment, including digging, trenching, blasting, boring, drilling, hammering, post driving, wrecking, razing, tunneling, or pavement or
concrete slab removal within 100 feet of an underground utility facility.

## Slide 5: Definition of “Excavation Activities”
30 V.S.A. § 7001(4) cont’d
Excavation activities shall NOT include the tilling of the soil for agricultural purposes, routine home gardening with hand tools outside easement areas and public rights-of-way, activities relating to routine public highway maintenance, or the use of hand tools by a utility or locator to locate or service facilities, provided the utility has a written damage prevention program.

## Slide 6: Public Utility Commission Rule 3.800 - Definitions
"Routine highway maintenance“ shall include:
Snow removal
Patching
Salting
Grading
Other day to day operations
BUT NOT
Ditching
Signpost setting
Guardrail placement or removal
Culvert work
Operations which do not disturb the subsurface of the earth, or which involve only the replacement of a post in the same location, shall be deemed to be routine.

## Slide 7: 30 V.S.A. § 7004 Notice of Excavation Activities
No person or company shall engage in excavation activities, except in an emergency situation, without pre-marking the proposed area of excavation activities and giving notice as required by this section.
Prior to notifying Dig Safe, the person shall pre-mark the area of proposed excavation activities in a manner that will enable operators of underground facilities to identify the boundaries of the proposed excavation activities.

## Slide 8: 30 V.S.A. § 7004 Notice of Excavation Activities
(c) At least 72 hours, excluding Saturdays, Sundays, and legal holidays, but not more than 30 days before commencing excavation activities, each person required to give notice of excavation activities shall notify Dig Safe, and shall contain a reasonably accurate and readily identifiable description of the geographical location of the proposed excavation activities and the pre-marks.

## Slide 9: 30 V.S.A. § 7004 Notice of Excavation Activities
(e) Notice of excavation activities shall be valid for an excavation site until one of the following occurs:
  the excavation is not completed within 30 days of the notification;
  the markings become faded, illegible, or destroyed; or
  the company installs new underground facilities in a marked area still under excavation.

## Slide 10: 30 V.S.A. § 7006 Marking of Underground Utility Facilities
The utility is required to mark facilities within 72 hours (not including Saturdays, Sundays, and legal holidays) of the receipt of the notice, marking the approximate location of its underground utility facilities in the area of the proposed excavation activities ….
Note: “Approximate location of underground utility facilities” means a strip of land extending not more than 18 inches on either side of the underground utility facilities. [30 V.S.A. § 7001(7)]

## Slide 11: Legal Holidays
Any legal holiday which falls on a Saturday shall be observed on the preceding Friday.
Any legal holiday which falls on a Sunday shall be observed on the following Monday.

## Slide 12: 30 V.S.A. § 7006a Maintenance of underground utility facility markings
After utilities have marked underground facilities, the excavator is responsible for maintenance of the markings.
In the event markings are obliterated, destroyed, or removed, the excavator MUST notify Dig Safe that remarking is needed.
The utility must remark within 72 hours, excluding of Saturdays, Sundays, and legal holidays.

## Slide 13: 30 V.S.A. § 7006b Excavation area precautions
Any person engaged in excavating activities near marked underground utilities must take reasonable precautions to avoid damaging underground utilities. The excavator must expose underground utilities to verify their location and depth, at each location where the work will cross a facility and at reasonable intervals when paralleling an underground facility. Powered or mechanized equipment may only be used near facilities that have been verified.

## Slide 14: 30 V.S.A. § 7007 Notice of Damage - Excavators
When any underground utility is damaged during excavation, the excavator shall immediately notify the affected company. Under no circumstances shall the excavator backfill or conceal the damaged area until the company inspects and repairs the damage and shall take reasonable and prudent actions to protect the public from serious injury from the damaged facilities until the company or emergency response personnel arrive.
An excavator who damages a natural gas line resulting in a release of gas shall promptly report the release to emergency responders by calling 911.

## Slide 15: PUC Rule 3.805(C) Notice of Damage - Utilities
Upon discovery of damage to underground facilities by excavation activities or other action that may constitute a probable violation, a utility shall submit an Underground Facility Damage Prevention Report.
Required for utilities
Optional for excavators

## Slide 16
Underground Facility Damage Reports (UFDR)
https://publicservice.vermont.gov/

## Slide 17
Underground Facility Damage Reports (UFDR)
UPLOAD
DOWNLOAD, COMPLETE & SAVE
https://publicservice.vermont.gov/regulated-utilities/engineering/underground-utility-damage-prevention-uudp-dig-safe-r

## Slide 19: Underground Facility Damage Reports (UFDRs)

## Slide 20: Civil Penalties
30 V.S.A. § 7008: Any person or company who violates any provisions of section 7004, 7006, 7006a, 7006b, or 7007 of this title shall be subject to a civil penalty of not more than:
  $500 for the first offense,
  $1,000 for the second offense within one year of the date of the first offense,
  $1,500 for the third offense within one year of the first offense, and
  $5,000 for the fourth or subsequent offense within one year of the date of a previous offense
PUC Rule 3.807(J): In imposing a civil penalty on any person, the Commission shall consider the gravity of the violation, the culpability of the person responsible for the violation, any history of prior violations, the good faith of the person in attempting to achieve compliance, the size of the business of the person being charged, the likely deterrent effect of the penalty, and any other relevant or mitigating factors.

## Slide 21: Bill Jordan Director of Engineering (802) 522-3959 Bill.Jordan@vermont.gov Lindsey Wells Admin. Services Coordinator (802) 261-5733 Lindsey.Wells@vermont.gov
Contact Information