## Slide 1
Rhode Island MUST Seminar
(Managing Underground Safety Training)
Ken Soares
Sr. Safety Professional
Rhode Island Energy
Contractor Electrical Safety
2024

## Slide 2
Keeping Contractors, Customers and our Employees Safe, is our Top Priority – ONE PPL

## Slide 3
Working Around Electrical Facilities Safely

## Slide 4
Electrical Distribution System Components

## Slide 5
High Voltage Proximity Act
High Voltage Proximity Act
10 Foot Minimum Clearance around all Electric Lines.
(if you know the voltage of the line)
Be aware of your surroundings.

## Slide 6
Facility Identification & Insulators
23kV – 46kV
Transmission
13kV
Primary
2.4kV – 5kV
Primary & Street Ltg.
(up to 6k volts)
120V & 240V
Secondary
TRANSMISSION POST
INSULATOR
PRIMARY
INSULATORS

## Slide 7
Facility Identification & Insulators
High Voltage Conductors-7200v to ground and 13,200v between phase wires
Insulators keep the voltage from ground. The pole will conduct high voltage
Cutouts can be used to switch off the transformer by opening the fuse. The fuse will blow open if high current from a fault is detected
Transformers step down voltage and step up current. This could be reversed with back feed.

## Slide 8
All Downed Wires Must Be Considered
ENERGIZED & DEADLY
They will energize any object they contact even phone lines.
Survey the area closely.
Potential Conductors include; fences, gutters, antennas, railroad tracks, aluminum siding & guide rail.
Assume all lines are energized and keep yourself and your equipment AT LEAST 20 FEET away if you have not confirmed the lines actual voltage! (OSHA 1926.1407-1408)
Higher voltages require greater clearances.
Even low-voltage electric shock can be fatal.

## Slide 9
Consider
the equipment energized
Call
the electric utility
Drive
Have the operator drive / move the equipment away from the line if possible
Stay
Tell the occupants to stay in the equipment if it cannot be driven away
If Equipment Contacts a Powerline
Warn bystanders to stay away
until the electric utility says it’s safe

## Slide 10
If Equipment Contacts a Powerline
Warn bystanders to stay away
until the electric utility says it’s safe!

## Slide 11
Step & Touch Potential
Current Flow Effect
Milliamp (ma) = 1/1000 ampere
Properties of Electricity
15-20 (ma) range from an AED shock

## Slide 12
Underground Electric Facilities
  Duct Banks w/ multiple conduit (concrete/clay)
  Conduit (Steel and Plastic)
  Direct Buried Cables
  Man-Holes or Vaults
Damaged Pad-Mounted Equipment
Keep everyone back, call the utility, and protect exposures
The outside can become energized if damaged
Stay clear!

## Slide 13
Underground Electric Facilities
Look For:
Riser Poles/Pole Drops
Underground Vaults/Manholes/Handholes
Pad mounted transformers/Switches
It’s the LAW!

## Slide 14
Underground Electric Facility Identification
Suspect buried electric facilities when:
Poles have conduit
Transformers are in yards
Electric meters are fed by underground wires in conduit instead of overhead wires.
Use caution when digging or driving anything into the ground
Call 811 before digging to location of underground facilities marked.

## Slide 15
Substations
If your working near an electrical substation be sure you're looking for underground get-a way markings. Distribution lines coming out of the substation are at a voltage of 13kV or more. Soft Vacuum excavation is encouraged in these areas.
Substations take high voltage and step it down to voltages used inside of homes

## Slide 16
Remember, if the circuit is not:
De-energized
Locked/tagged out
Tested and grounded
Varies from no lasting affect to sever burns and fatalities
Effects of Electricity On the Body
IT’S NOT DEAD!

## Slide 17
Never attempt to disconnect or reconnect electrical services:
Never cut service wires
Never attempt to remove electrical meters. Failures during removal can be catastrophic
Removed meters will NOT de-energize all types of electric service
Electric Meters

## Slide 18
In case of emergency, call 911
Rhode Island Energy (RIE)
1-855-743-1102 (1-855-RIE-1101)
For more safety info:
https://www.rienergy.com/RI-Home/Safety-Outages/safety-outages
Contact information

## Slide 19
MUST Seminar 2024
QUESTIONS?